## Slide 1: IPv6-only at Microsoft
Marcus Keane
Network Architect
Microsoft
Microsoft IT

## Slide 2: Agenda
Network Overview
IPv6 Dual-Stack Status
The move to IPv6-only
Problems encountered
Future directions

## Slide 3: Network Overview
Main Redmond campus - 100+ Buildings
Three regions with smaller campuses and tail sites
  EMEA, Asia and North America
10+ On-premise data centres
Most tail-site WAN is carrier MPLS
775+ locations in total
~1.2m devices hitting the network

## Slide 4: IPv6 Dual-Stack Status
First configured on network in 1993
More broadly deployed in 2006 using mixture of ISATAP and native
Internet peering enabled in US and regions
  Mostly with AS8075
All new networks deployed with IPv6
Recent retrofit pushed native to all corporate networks
Labs and co-managed networks now in scope

## Slide 5: IPv6-Only – why?
Exhaustion of IPv4 space – including RFC1918 space
Overlapping RFC1918 space
  Azure
  Acquisitions
Operational complexity of dual-stack
Strategic Goal

## Slide 6: IPv6-only – part 1
Two test networks in Seattle
  Wireless Guest
  Wired and wireless network on the corporate network
Both networks opt-in
Non-redundant NAT64/DNS64
Tested different address acquisition schemes
  SLAAC on wireless guest
  DHCPv6 stateful and SLAAC for the corporate network
For guest network - DHCPv6 stateless + RDNSS

## Slide 7: IPv6-only – part 2
Target production networks
Initial focus on wireless guest
Rebuilt network to current redundancy standards
  VRRP
  Redundant NAT64/DNS64
Extended network to other buildings on campus

## Slide 8: Problems – DNS resolver
DNS name resolution
  Windows only supports DHCPv6
  Android only supports RDNSS
Need to support both
Parallel DHCPv6 infrastructure
Not all routers support RDNSS
  Platform support coming
Solution – centralised default gateway
  L2VPN(EVPN) overlay
  Run RDNSS and DHCPv6 relay on central router pair

## Slide 9
EVPN
Trunk(752)
Trunk(752)
Trunk(900)
Default Gateways
VRRP
Q-in-Q on subinterfaces
RDNSS + DHCPv6 Relay
Building switches
Impose Q-in-Q tag
Building Routers
Hub Routers

## Slide 10: Some issues remain…
Most WAN connectivity is carrier L3VPN
  MPLS EVPN not possible
  VXLAN a possibility in sites with supporting hardware
Some LAN routers will never support RDNSS
  We can use centralised DG model but…
  These devices don’t support EVPN either.
  A solution with pseudowires is a possibility.
  Redundancy is tricky

## Slide 11: Existing status
Redmond test equipment being replaced by production equipment
NAT64/DNS64 being deployed in Europe
Single centralised DG deployed for RDNSS support
  Redmond
  Europe

## Slide 12: Future Plans
Deploy redundant NAT64/DNS64 to other regions
Expand centralised DG solution to the other regions
Start piloting IPv6-only on corporate networks
  Redmond and Europe probably first targets
Start thinking about our Internet First strategy
  This will require a rethink of NAT64/DNS64.

## Slide 13: Questions?