## Slide 1: SoloWAN: open source WAN optimization
David Fernández, F. Javier Ruiz, Luis Bellido, Raúl Álvarez, German Martín, Carlos Vega, Roberto Montero, Mattia Peirano, Francisco Huertas, Antonio Celorio, Juan Carlos Dueñas
solowan@dit.upm.es
Center for Open Middleware
Universidad Politécnica de Madrid
Universidad Politécnica de Madrid (UPM)

## Slide 2: Contents
WAN optimization techniques
SoloWAN project
Use case scenarios and results
Virtual testbeds scenarios based on VNX
Notes: Software libre para la optimización WAN (4m)
  Mencionar WanOS, aunque fuera del estudio inicial
OpenNOP-SoloWAN (8m)
  Características. Arquitectura. Docker.
  Pruebas y resultados (BBDD, WanOS, WCCP)
Entornos virtuales de pruebas: VNX (3m)
Arquitectura escalable (5m)
  Balanceador SDN
  Pruebas y resultados (WCCP)
Resumen de logros (2m)
Conclusiones y trabajos futuros (3m)

## Slide 3: WAN Optimization Techniques
Objective: improve WAN links performance
  WAN link characteristics: lower bandwidth, higher delays, higher cost
Techniques:
  Compression, Deduplication (or dictionary based compression), TCP optimization, Application caches, etc.
WAN
Data Center A
Data Center B

## Slide 4: WAN optimization based on deduplication
WOC B Dictionary/cache
WOC A Dictionary/cache
WAN
Data Center A
Data Center B
WOC
WOC
WAN Optimization Devices
Notes: New algorithms, such as dictionary based compression, also known as deduplication, use a different approach to further reduce the redundancy among different connections. (10s)
(CLICK) Basically, every packet transmitted is stored in a dictionary in both optimizers. (5s)
~17 s

## Slide 5: WAN optimization based on deduplication
WOC B Dictionary/cache
WOC A Dictionary/cache
WAN
Data Center A
Data Center B
WOC
WOC
Redundancy
info block detected
Info block replaced by a short symbol (hash)
Notes: (CLICK) Whenever a new packet arrives at the inbound optimizer, the dictionary is scanned (CLICK) to find blocks of information that have already been transmitted. If found (CLICK), these blocks are substituted by a short symbol or hash, thus reducing the volume of information transmitted. (16 s)
~18 s

## Slide 6: WAN optimization based on deduplication
WOC B Dictionary/cache
WOC A Dictionary/cache
WAN
Data Center A
Data Center B
WOC
WOC
Original
info block recovered
Original
info block recovered
Notes: (CLICK) When the packet arrives at the outbound optimizer, the hash is replaced by the original information before forwarding it to its final destination. (10 s)
~12 s

## Slide 7: SoloWAN rationale
Commercial WOC solutions:
  Complex systems
  Scalability and elasticity issues
  High cost in terms of equipment and licensing
What about open source software (OSS) based WAN optimization solutions?
Notes: Ver informe de Gartner: “Magic Quadrant for WAN Optimization”

## Slide 8: SoloWAN initial objective
Evaluate the use of Open Source Software (OSS) for WAN optimization in the context of corporate communications
  Study of available solutions
  Creation of virtual and real testing environments
  Test OSS solutions and conclude recommendations
Objective reoriented to enhance OSS OpenNOP WAN optimization platform with:
  Efficient deduplication algorithm
  Scalable and elastic architecture running on standard hardware
Any OSS mature solution found?
YES
NO
Notes: Ver informe de Gartner: “Magic Quadrant for WAN Optimization”

## Slide 9: SoloWAN Architecture
Based on Open Network Optimization Platform (OpenNOP, www.opennop.org)
Linux kernel module + application in user-space
Use of netfilter to capture traffic
Multithread (worker)
Written in C
Linux
Kernel
Linux
User Space

## Slide 10: Deduplication Algorithm
Deduplication functionality based on:
  Neil T. Spring and David Wetherall. A Protocol-Independent Technique for Eliminating Redundant Network Traffic. SIGCOMM '00.
Main problem: how to efficiently identify repeated content?
  Computationally intensive
Transmitted packet cache
New packet to Tx
=
?
Simplification:
  Compare only fixed size blocks (64 bytes) at a reduced number of positions (32)
  Calculate a hash (fingerprint) for each block inside a packed and store it in the dictionary together with the packet
  Once a match is detected, look around matching block to see if more bytes match

## Slide 11: SoloWAN characteristics
Algorithms:
  Compression (originally included in OpenNOP)
  Deduplication
  Deduplication + Compression
Available as a linux daemon or as a docker container
First version released in nov 2014
  https://github.com/solowan/solowan
Multithread architecture with dictionaries shared among threads
Demo virtual machine available with VNX based virtual scenarios
Wireshark Plugin to decode SoloWAN packet format

## Slide 12: SoloWAN Scenarios
  Optimizer-in-the-Network (oitn)
  End-to-End (e2e)
WAN
Optimizer1
Optimizer2
WAN
R1
R2
h1
Application
Opennopd
h2
Application
opennopd
Process or docker container

## Slide 13: SoloWAN Tests
Mainly tested with FTP, HTTP and access to mysql databases
  Not suitable for encrypted traffic
Using benchmark files from Silesia Corpus:
  Set of representative files (de 6 a 51 M)
  http://www.data-compression.info/Corpora/SilesiaCorpus/

## Slide 14: Web application interface
Limited management and real time statistics:

## Slide 15: SoloWAN in German IT press
SoloWAN in the popular German enterprise IT magazine:
iX - Magazin für Professionelle Informationstechnik
Article about open source based WAN optimization solutions:
  OpenNOP
  SoloWAN
  TrafficSqueezer
  Wanproxy
Includes laboratory tests:
  Highlights the easy installation and high compression rate provided by SoloWAN

## Slide 16: SoloWAN Scenarios
Traffic redirection based on WCCPv2
WAN
Optimizers
Optimizers
LAN 2
LAN 1
h1
h3
h2
h4
h6
h5
o1
Router 1
Router 2
WCCP
o2
WCCP
WAN
Notes: Los optimizadores o1 y o2 envían un mensaje WCCP a los routers para indicar redirección del tráfico deseado (en este caso todos los paquetes cuyo puerto origen o destino sea el 80)
Los optimizadores procesan los paquetes y lo reenvían a su destino.
16

## Slide 17: SoloWAN cloud architecture
Create a scalable architecture based in SoloWAN with support for multiple parallel optimizers
  Multiple threads per machine
  Multiple servers
Use cloud computing paradigms to add optimizers as needed
LAN
Traffic Load Balancer
(SDN based)
LAN
O1
O2
O3
D1
D2
D3
O4
D4
Easy
expansion(plug&play)
Optimizer

## Slide 18: SDN based SoloWAN cloud architecture
Reference and testbed scenario:
LAN B
LAN A
h11
h13
h12
h21
h23
h22
lb1
o11
o12
o13
Floodlight OpenFlow Controllers
lb2
o21
o22
o23
Router 1
Router 2
WAN
WAN Optimizer
WAN Optimizer
Notes: Configuración de los optimizadores:
    thrnum 1
    num_pkt_cache_size 262144
    pkt_size 1500
    fp_per_pkt 32
    fps_factor 2
  Ocupación en memoria de cada optimizador: 3 GBs (fórmula: 2 x thrnum x num_pkt_cache_size x (pkt_size + 64 x fp_per_pkt x fps_factor).
  Limitación de CPU al 25% para cada optimizador.
  Se comparará dos modos de optimización:
    Solo deduplicación
    Combinada: Deduplicación + Compresión.
Ficheros de pruebas: Silesia Corpus.
  Se trata de un conjunto de ficheros que engloban los tipos de datos típicos usados hoy en día:
  Tamaño: 211 MBs.
Transferencias:
  h21 -> h11
  h22 -> h12
  h23 -> h13

## Slide 19: Scalable architecture Tests

## Slide 20: WAN Optimization as a Service
Idea: Integrate WAN optimization as a service available in Openstack IaaS
Proof of Concept implementation developed
  https://github.com/carlosv5/OaaS-network
Based on Firewall as a Service (FWaaS) Openstack code

## Slide 21: Typical Openstack Scenario
network
compute2
compute1
controller
Management Network
Tunnel Network
External Network
eth1
eth1
eth1
eth1
eth2
eth2
eth2
eth3
eth2
Internet
Virtual Network
Sw
Sw
vm3
vm4
vm5
vm1
vm2
Router
NAT

## Slide 22: WAN Optimization as a Service
network
compute2
compute1
controller
Management Network
Tunnel Network
External Network
eth1
eth1
eth1
eth1
eth2
eth2
eth2
eth3
eth2
Internet
Virtual Network
Sw
Sw
vm3
vm4
vm5
vm1
vm2
Router
NAT
FWaaS
LBaaS
WOaaS

## Slide 23: WOaaS Complete Test Scenario (I)
network
compute1
controller
Management Network
Tunnel Network
External Network B
eth1
eth1
eth1
eth2
eth2
eth3
eth2
Cloud B
Basic scenario tested over two Openstack clouds
network
compute1
controller
Management Network
Tunnel Network
eth1
eth1
eth1
eth2
eth2
eth3
eth2
Cloud A
External Network A
WAN
O1
O2
h1
h2
GRE tunnel
Virtual Network
h2
Router
NAT
WOaaS
Virtual Network
h1
Router
NAT
WOaaS

## Slide 24: WOaaS Complete Test Scenario (II)
Virtual Scenario A
Virtual Scenario B
Testing infrastructure:
network
compute1
controller
Management Network
Tunnel Network
External Network B
eth1
eth1
eth1
eth2
eth2
eth3
eth2
Cloud B
network
compute1
controller
Management Network
Tunnel Network
eth1
eth1
eth1
eth2
eth2
eth3
eth2
Cloud A
External Network A
GRE tunnel
Virtual Network
h2
Router
NAT
WOaaS
Virtual Network
h1
Router
NAT
WOaaS
Switch
LaptopA
LaptopB

## Slide 25: WAN Optimization as a Service
network
compute2
compute1
controller
Management Network
Tunnel Network
External Network
eth1
eth1
eth1
eth1
eth2
eth2
eth2
eth3
eth2
Internet
vm3
vm4
vm5
Sw
vm1
Sw
Router +
WAN optimizator
NAT
Virtual Network
vm2

## Slide 26: Virtual Testbeds
Most SoloWAN testbeds developed using virtual testbeds based on VNX tool
Combining VM and virtual network emulation on the host it is possible to run Virtual Network Scenarios
Internet
Net 1
Net 2
Net 3
Net 4
Real Scenario
Host
Virtual Scenario
Internet
Virtual
Networks
Net2
Net1
Net4
Net3
Virtual nodes
VNX tool
http://www.dit.upm.es/vnx
Notes: 26

## Slide 27: VNX: Virtual Networks over LinuX
VNX is a general purpose open-source virtualization tool designed to help building virtual network testbeds automatically
Characteristics:
  Uses libvirt (Linux virtualization library)
  Autoconfiguration for Linux, FreeBSD, OpenBSD and Windows
  Support for Dynamips (CISCO) and Olive (Juniper)
  LXC containers support
  Open vSwitch support
http://www.dit.upm.es/vnx
Specification
Design
Creation
Interaction

## Slide 28: SoloWAN Demo VM
Ubuntu VM including SoloWAN virtual scenarios
Available at: https://goo.gl/YE6QXW

## Slide 29: VNX Example scenario: Collaborative OSPF/BGP Practice
Requirements for ~400 students:
Backbone: 15 dynamips routers, 5 servidores
Cient networks : 400 x 5 routers Linux with quagga routers, 4 PCs
Switches
Configuration management
  400 different configurations

## Slide 30: References
Center for Open Middleware (COM).
  http://www.centeropenmiddleware.com/
SoloWAN repository at Github.
  https://github.com/solowan/solowan
Virtual Networks over Linux (VNX).
  http://vnx.dit.upm.es
WOaaS Prof-of-concept implementation.
  https://github.com/carlosv5/OaaS-network

## Slide 31: Thanks for your attention Any questions?
Universidad Politécnica de Madrid (UPM)